## Slide 1
RETURN PERIOD HYDROGRAPHS
TEAM 11
First week’s presentation

## Slide 2
QUESTION?
How to produce 10y , 20y, 50y and 100y return period hydrographs estimation and associated flooded areas in the Var low valley?
How to use IDF curves? Analysis should focus on hydrological part and only simple hydraulic modeling can be used for the low valley for the different scenarios.

## Slide 3
WORKFLOW

## Slide 4: CATCHMENT CHARACTERISTICS

## Slide 5
Var catchment is located in the south of France with a total area of about 2822 km².
It is composed of five sub-catchments.
Notes: •Upper var with the area about 1087.47 km² is the biggest sub-catchment.

## Slide 6: DATA PREPARATION USING IDF CURVE

## Slide 7: Data preparation using IDF curve
Montana equation: I = a X t -b
I = Intensity (mm/hr)
t = duration (hr)
a & b = local coefficient statistically calculated
by Meteo France based on
measurement data from 1966 – 2012
a & b values for various return periods
Chart: IDF Curve : 10 Yrs return period
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.5 | 19 | 19.5 | 20 | 20.5 | 21 | 21.5 | 22 | 22.5 | 23 | 23.5 | 24
 | 57.0958 | 15.5502 | 10.992 | 8.7935 | 7.4526 | 6.5331 | 5.8559 | 5.3325 | 4.9134 | 4.5689 | 4.2797 | 4.0327 | 3.819 | 3.6318 | 3.4662 | 3.3186 | 3.1858 | 3.0658 | 2.9566 | 2.8567 | 2.7649 | 2.6803 | 2.6019 | 2.5291 | 2.4613 | 2.3978 | 2.3384 | 2.2825 | 2.23 | 2.1803 | 2.1334 | 2.089 | 2.0468 | 2.0067 | 1.9686 | 1.9322 | 1.8975 | 1.8643 | 1.8326 | 1.8022 | 1.773 | 1.745 | 1.7181 | 1.6922 | 1.6673 | 1.6433 | 1.6201 | 1.5978
Coefficients | 10 Yrs | 20 Yrs | 50 Yrs | 100 Yrs
a | 36.32 | 40.09 | 45.07 | 97.50
b | 0.65 | 0.65 | 0.65 | 0.82

## Slide 8: Data Preparation : with IDF curve
Hyetograph obtained using alternative block method.
Objective is to construct hyetograph such that peak precipitation occurs in the middle of the storm
One of the recommended approaches to generate design storm among others (Sifalda and linear / exponential models)
Used as input for HEC-HMS
Chart: Hyetograph
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
 | 0.81 | 0.835 | 0.86 | 0.885 | 0.915 | 0.95 | 0.985 | 1.025 | 1.065 | 1.115 | 1.17 | 1.23 | 1.3 | 1.38 | 1.48 | 1.595 | 1.735 | 1.91 | 2.14 | 2.455 | 2.93 | 3.725 | 5.495 | 28.55 | 7.775 | 4.395 | 3.265 | 2.665 | 2.285 | 2.015 | 1.815 | 1.66 | 1.535 | 1.43 | 1.34 | 1.265 | 1.2 | 1.14 | 1.09 | 1.045 | 1.005 | 0.965 | 0.93 | 0.9 | 0.87 | 0.845 | 0.82 | 0.8

## Slide 9: HYDROLOGICAL MODELLING
HEC-HMS

## Slide 10: Hydrological modelling
HEC-HMS used for hydrological modelling.
Model setup:
    5 sub-catchments, 3 junctions and 3 reaches
    1 precipitation gage introduced, with 30 minutes interval
    data for 24 hours
    Catchment Parameters:
Peak discharge for 10 years return period : 6113 cms
Sub Basin | Curve Number | Imperviousness
Upper Var | 77 | 20
Tinee | 75 | 21
Esteron | 72 | 13
Vesubie | 73 | 17
Lower Var | 72 | 24

## Slide 11: Hydrological modelling
Modification of the catchment parameters:
Peak discharge for various return periods
Return Period | Peak discharge (cms)
10 | 1700
20 | 2058
50 | 2557
100 | 4369

## Slide 12: Results from Hydrological Modelling
Chart: Hydrographs from IDF curve method
Rainfall data depends upon the local coefficients. Hence, the representation of rainfall can be less accurate

## Slide 13: DATA PREPARATION USING RAINFALL GENERATOR

## Slide 14: Data Preparation with rainfall generator
Unit hyetograph
Used as input rainfall data for HEC-HMS

## Slide 15: HYDROLOGICAL MODELLING
HEC-HMS

## Slide 16: Hydrological Modelling
Return Period | Peak discharge (cms)
10 Years | 1720
20 Years | 2096
50 Years | 2640
100 Years | 3114
Chart: Hydrographs - rainfall data from rainfall generator
Rainfall data are more representative of historical patterns, hence the hydrographs are more accurate

## Slide 17: Flood Frequency Analysis

## Slide 18: Methods
Gumbel distribution
XT = µ + K ∗ σ
K =
u =
XT = Gumbel’s distribution K = frequency factor μ = mean σ = Standard deviation a = μ – b * euler constant b = σ *sqrt(6)/ π
Normal Distribution
u =
The return period (T) of an event is defined as the inverse of the occurrence rate.
= discharge values of sample size
T = return period

## Slide 19: Procedure
Monthly peak flood data was assembled from 1975-2018 and 1994.
We sort the discharge data in increasing order.
We assign ranks to each value.
Calculate the probability of non-exceedance with Hasan’s formula:
𝐹 () = 𝑟 − 0.5 /𝑛
Graphical representation of against the peak discharges.

## Slide 20: Flood analysis by Gumbel’s Distribution
Return period (years) | Frequency (%) | Reduced Variate(u) | Discharge(m3/s) (1975-2018) | Discharge (1994)
10 | 99.17 | 4.79 | 710.01 | 1672.1
20 | 99.59 | 5.48 | 804.24 | 1900.06
50 | 99.83 | 6.40 | 928.6 | 2201
100 | 99.92 | 7.08 | 1022.6 | 2428.4

## Slide 21: Flood frequency for 1975-2018
Gumbel (1975-2018)
Normal (1975-2018)

## Slide 22
Flood analysis by Normal distribution
Return period (years) | Frequency (%) | Reduced Variate(u) | Discharge (1975-2018) | Discharge (1994)
10 | 99.17 | 4.79 | 556.1 | 1299.7
20 | 99.59 | 5.48 | 598.6 | 1402.43
50 | 99.83 | 6.40 | 650.17 | 1527.3
100 | 99.92 | 7.09 | 686.46 | 1615.1

## Slide 23
Normal (1994)
Flood frequency for 1994
Gumbel (1994)

## Slide 24
FLOOD EXTENT
HYDRAULIC MODELLING (TELEMAC 2D)

## Slide 25
Covers the area from the La Manda bridge to the airport
5m DEM resolution
Mesh resolution of 5m in the minor river bed, 50m in the major bed and up to 400m for the rest of the model
Model characteristics
Notes: TELEMAC-2D solves the depth-averaged Navier-Stokes equation utilizing both Finite-Element (FE) and Finite-Volume (FV) formulations. All of these formulations require that a spatial representation of the domain be created using a computational mesh.

## Slide 26
Simulations
Notes: TELEMAC-2D simulation parameters ﬁle (*.cas) (inflow hydrograph)

## Slide 27
Results
Flood extend for the flood analysis method’s 10 years return period, 3h15 after the hydrograph peac
Flood extend for the flood analysis method’s 20 years return period, 3h25 after the hydrograph peac
Notes: TELEMAC-2D simulation parameters ﬁle (*.cas) (inflow hydrograph)

## Slide 28
Results
Flood extend for the flood analysis method’s 50 years return period, 3h44 after the hydrograph peac
Flood extend for the flood analysis method’s 100 years return period, 3h44 after the hydrograph peac
Notes: TELEMAC-2D simulation parameters ﬁle (*.cas) (inflow hydrograph)

## Slide 29
Summary
Data generated from rainfall generator can be considered more accurate as compared to data generated from IDF curves, and hence produce better hydrographs.
Gumbel’s distribution is a better analysis method for extreme cases, in our case flood analysis.

## Slide 30: References
Gumbel, E.J. (1935), "Les valeurs extrêmes des distributions statistiques" (PDF), Annales de l'Institut Henri Poincaré, 5 (2) : 115–158.
A. Hazen et G.S. Williams, Hydraulic Tables, New York, John Wiley and Sons, 1920, 3e éd.

## Slide 31: Thank You